Input Data for structural analysis

of application buried pipes in open trench condition,

calculation acc.  DWA-A 127

Please send to:

Amiblu Holding GmbH

Pischeldorfer Straße 128

A-9020 Klagenfurt

T +43 463 482424

info@amiblu.com

|  | Text input. |
| --- | --- |
|  | project |  |  |
|  | Text input. |  | Text input. |
|  | company |  | contact person |
|  | Text input. |  | Text input. |
|  | street |  | phone/Fax: |
|  | Text input. |  | Text input. |
|  | postcode |  | signature: |
|  | Text input. |  | Text input. |
|  | city |  | date/stamp |

Pipe Details:

| nominal diameter DN | Text input. |  | sewer pipe |  |
| --- | --- | --- | --- | --- |
|  |  |  | sewer pressure pipe |  |
| pressure class PN | Text input. |  | pressure pipe |  |
|  |  |  | potable water pipe |  |
| nominal stiffness SN | Text input. |  | installation in protective water area |  |
|  |  |  | air pipe |  |
| pipe material | GRP |  | storage sewer |  |
|  |  |  | others | Text input. |

Types of native soil: 	acc. ATV-DVWK-A 127; DIN 18196          			(please subsoil expertise ad)

|  |  | Native soil | backfilling | Pipe zone |
| --- | --- | --- | --- | --- |
| G1 | Non cohesive soils (gravel, sand) (GE, GW, GI, SE, SW, SI) |  |  |  |
| G2 | Slightly cohesive soils (GU, GT, SU, ST) |  |  |  |
| G3 | Cohesive mixed soils, silt (GŪ, GŤ, SŪ, SŤ, UL, UM) |  |  |  |
| G4 | Cohesive soils, except silts (TL, TM, TA, OU, OT, OH, UA) |  |  |  |
| Other types of soil | Text input. |  |  |  |

| Proctor density for native soil | Text input. | % |  |
| --- | --- | --- | --- |
| (Proctor density 85 – 100 %) |  |  |  |

| Foundation of pipeline | On native soil |
| --- | --- |
|  | very hard and rocky |
|  | Weak soil, not stable for foundation |
|  | Soil replacement: thickness Text input. m |
|  | material Text input. |
|  | Proctor density DPr Text input. % |

Specification of loads:

|  | Min. cover depth |  | Max. cover depth |  |
| --- | --- | --- | --- | --- |
| Depth of earth cover h | Text input. | m | Text input. | m |
| min. Ground water hw above pipe invert | Text input. | m | Text input. | m |
| max. Ground water hw above pipe invert | Text input. | m | Text input. | m |

| Other surface loads | Text input. | kN/m² |  |  |
| --- | --- | --- | --- | --- |
| For pressure pipes | Short term | Text input. | bar, e.g. system test pressure; hydrostatic pressure, water hammer |
|  | Long term | Text input. | bar, e.g. operating pressure (OP), system pressure (PN, DP) |
| Traffic load | no traffic |  |  |  |
|  | street |  | railway | aircraft |
|  | HCL 60 |  | one track, UIC | BFZ 90 |
|  | HCL 30 |  | two tracks, UIC | BFZ 180 |
|  | HGV 12 |  | one track, LM 71 | BFZ 350 |
|  | DIN EN 1991-2, TS und UDL | two tracks, LM 71 | BFZ 550 |
|  | LM1-lane 3,00 m |  | BFZ 750 |
|  | LM1-lane 2,70 m |
|  | LM1-green field area |
|  | Other loads, e.g. special vehicle (please add load scheme with axle, wheels and wheel loads): |
|  | Text input. |

Building construction:

Type of trench	    embankment                 single trench               double trench 1)           stepped trench 1)

1) For special shapes add a sketch

Text input.

Trench angel    90°                 60°               45°

Text input.

Width of trench    b =                                              m at pipe crown

Text input.

bSo =                                           m at pipe trench bottom inclusive planks

| Trench planking no planks Horizontal planks, also applies to plank walls (Berlin lining) Planking with plates Vertical plank with light weight Vertical plank with boards * Vertical plank with light weight * Vertical plank with sheet piling * | bedding on native soil (acc. EN 1610) on gravel, sand on concrete 2) 2) only as spezial construction in agreement with the pipe producer bedding 90° 120° angle 2α 180° |
| --- | --- |
| * Depth of sheeting below pipe invert | tS = | Text input. | m |
| *thickness of plank (one-side) | bS = | Text input. | m |

Cover condition for backfilling:

A1	Backfilling compacted in layers against the native soil (without proof of compaction degree);

also applies to plank walls, Berlin lining

A2	Vertical pipe trench lining with boards that are not removed before backfilling.

Lining boards or devices that are removed step by step during backfilling. Non-compacted

backfilling/ backfilling with slurry (only suitable for soils of group G1).

A3	Vertical trench lining with sheet piling, light weight sheet connection, wooden planks, lining

boards or devices that are not removed before backfilling.

A4	Backfilling compacted in layers against the native soil with proof of the required compaction

degree to ZTVE-StB ; also applies to plank walls (Berlin lining). Cover condition A4 is not

applicable to sails of group G4.

Bedding condition for pipe:

B1	Bedding compacted in layers against the native soil or in the embankment (without proof of

compaction degree); also applies to plank walls, Berlin lining

B2	Vertical lining in the pipe zone with planks that reach down to the trench bottom and are not

removed before backfilling and compaction. Lining boards or devices provided that the soil

is compacted after the linings are removed.

B3	Vertical lining in the pipe zone with sheet piling or lightweight sheeting and compaction against

the lining reaching down below the trench bottom. There is no safe calculation model for

determining vertical lining with wooden planks, boards or devices that are not removed before

backfilling and compaction the pipe zone.

B4	Bedding compacted in layers against the native soil or in the embankment with proof of the

required compaction degree to ZTVE-StB. Bedding condition B4 does not apply to soils of

group G4.